## Slide 1
GTU | PROBLEM-BASED LEARNING (PBL) | FINAL PRESENTATION
Design and Development of a Fuzzy Logic-Based Automatic Braking System
Mamdani Fuzzy Inference System in Python (scikit-fuzzy)
Subject: Fuzzy Logic and Genetic Programming (BE05000461)
Department: Automobile Engineering
Institute: L.D. College of Engineering (LDCE), Ahmedabad
University: Gujarat Technological University (GTU)
Darshan Kantibhai Prajapati (Enrollment No: 250283102033)
Parth Sanjaybhai Parmar (Enrollment No: 250283102028)
Faculty Guide: [Name] | Academic Year: [Academic Year] | Date: [Date]
D (m)
Vc (m/s)
Ego vehicle
Vehicle ahead
Inputs: D and Vc → Fuzzy controller → Braking command B (0–100 %)
Illustrative schematic only – not project evidence
Notes: Introduce project, team, and subject. Educational software simulation.

## Slide 2: Problem Statement and Motivation
The problem
Drivers can react late to a closing obstacle because of distraction, fatigue or misjudged gaps. Braking decisions are vague: “near” and “fast” have no sharp boundary, which suits fuzzy logic better than crisp thresholds.
Why two inputs?
Distance alone ignores how quickly the gap is closing; speed alone ignores how much gap remains. A 20 m gap is relaxed at 2 m/s closing but urgent at 20 m/s. Together they approximate time-to-collision (TTC ≈ D / Vc).
Motivation and scope
Show how IF–THEN rules capture driver-like judgement and output a braking command (0–100 %). Scope: educational PBL software simulation. It does not claim to prevent collisions or replace production ADAS.
2
Inputs: D, Vc
1
Output: braking %
9
Fuzzy rules
Mamdani
Inference type

## Slide 3: Objectives and System Architecture
1
Define 2 inputs and 1 output with ranges and units
2
Design 9 triangular membership functions (3 per variable)
3
Build a 9-rule Mamdani rule base (brief requires ≥ 6–8)
4
Hand-calculate one worked example (D = 20 m, Vc = 15 m/s)
5
Implement in Python with scikit-fuzzy; test ≥ 10 input pairs
6
Analyse behaviour, limitations and improvements
Inputs
D (m), Vc (m/s)
Fuzzification
μ values
Rule evaluation
min (AND)
Aggregation
max
Centroid defuzzification
Braking command
B (0–100 %)
Fig. 1 – Mamdani FIS processing chain implemented in the simulation.
Simulation architecture only: no sensors, ECU, brake actuator or vehicle dynamics are modelled.

## Slide 4: Variables and Membership Functions
Variable | Role | Unit | Universe | Terms and triangular MF [a, b, c]
Obstacle distance D | Input 1 | m | 0–100 | Near [0,0,30] · Medium [10,40,70] · Far [50,100,100]
Closing speed Vc | Input 2 | m/s | 0–30 | Slow [0,0,10] · Moderate [5,15,25] · Fast [20,30,30]
Braking command B | Output | % | 0–100 | Light [0,0,40] · Moderate [20,50,80] · Hard [60,100,100]
Fig. 2 – Distance MFs
Fig. 3 – Closing-speed MFs
Fig. 4 – Braking-command MFs
Triangular MFs chosen for simplicity (Triangular / Trapezoidal / Gaussian allowed by brief). Edge-degenerate shapes suit a classroom demo; thresholds need engineering validation before real use.

## Slide 5: Mamdani Fuzzy Inference Methodology
1
Fuzzification
Crisp D and Vc → membership degrees μ in each linguistic term
2
Rule evaluation
Antecedents combined with AND = min; output set clipped at α (min implication)
3
Aggregation
Clipped output sets of all rules combined with max
4
Defuzzification
Centroid of the aggregated set gives crisp braking command B*
Rule firing strength
αᵢ = min( μAᵢ(D), μBᵢ(Vc) )
Centroid defuzzification
B* = ∫ b · μagg(b) db / ∫ μagg(b) db
Evaluated numerically on a 1 % grid (exact piecewise-linear centroid, as in scikit-fuzzy).
Symbols
αᵢ – firing strength of rule i
μAᵢ, μBᵢ – membership of D and Vc in rule i’s terms
μagg(b) – aggregated output membership at braking level b
B* – crisp braking command (%)
Operators: AND = min, implication = min, aggregation = max

## Slide 6: Fuzzy Rule Base (9 Rules)
Distance ↓ / Vc → | Slow | Moderate | Fast
Near | R1 Moderate | R2 Hard | R3 Hard
Medium | R4 Light | R5 Moderate | R6 Hard
Far | R7 Light | R8 Light | R9 Moderate
Table 1 – Rule matrix: IF Distance is … AND Closing speed is … THEN Braking is …
Design logic
Nearer obstacle and higher closing speed → stronger braking
Far obstacle with low closing speed → light braking
Near + Slow gives Moderate (not Hard): small closing rate leaves time to react
Far + Fast gives Moderate: high speed warrants early action
A simplified demonstration rule base: it does not guarantee safe or optimal braking and must be validated against stopping-distance and vehicle-dynamics data before any real-world use.

## Slide 7: Worked Example: D = 20 m, Vc = 15 m/s
Step | Calculation
Fuzzify D = 20 | Near = (30−20)/(30−0) = 0.333 Medium = (20−10)/(40−10) = 0.333 Far = 0
Fuzzify Vc = 15 | Slow = 0 · Moderate = 1 (peak) · Fast = 0
Rules fired | R2: Near ∧ Moderate → Hard α = min(0.333, 1) = 0.333 R5: Medium ∧ Moderate → Moderate α = min(0.333, 1) = 0.333 All other rules: α = 0
Aggregate | max of Hard clipped at 0.333 and Moderate clipped at 0.333
Defuzzify | Centroid of aggregated set (executed model) = 62.4 %
Fig. 5 – Aggregated output set and centroid from the executed model.
Why not a simple weighted average?
Averaging the label peaks (100 and 50) would give 75 %. The Mamdani centroid uses the full clipped shapes, so the true output is 62.4 %.

## Slide 8: Python Implementation (scikit-fuzzy)
import numpy as np
import skfuzzy as fuzz
from skfuzzy import control as ctrl
dist = ctrl.Antecedent(np.arange(0,101,1),'distance')
speed = ctrl.Antecedent(np.arange(0,31,1),'closing_speed')
brake = ctrl.Consequent(np.arange(0,101,1),'brake')
dist['Near'] = fuzz.trimf(dist.universe,[0,0,30])
dist['Medium'] = fuzz.trimf(dist.universe,[10,40,70])
dist['Far'] = fuzz.trimf(dist.universe,[50,100,100])
speed['Slow'] = fuzz.trimf(speed.universe,[0,0,10])
speed['Moderate'] = fuzz.trimf(speed.universe,[5,15,25])
speed['Fast'] = fuzz.trimf(speed.universe,[20,30,30])
brake['Light'] = fuzz.trimf(brake.universe,[0,0,40])
brake['Moderate'] = fuzz.trimf(brake.universe,[20,50,80])
brake['Hard'] = fuzz.trimf(brake.universe,[60,100,100])
rules = [
ctrl.Rule(dist['Near'] & speed['Slow'],
brake['Moderate']), # R1
ctrl.Rule(dist['Near'] & speed['Moderate'],
brake['Hard']), # R2
# ... R3 - R8 as in rule table ...
ctrl.Rule(dist['Far'] & speed['Fast'],
brake['Moderate']), # R9
]
system = ctrl.ControlSystem(rules)
sim = ctrl.ControlSystemSimulation(system)
sim.input['distance'] = 20
sim.input['closing_speed'] = 15
sim.compute()
print(sim.output['brake']) # centroid
Defaults in scikit-fuzzy: AND = min, aggregation = max, Consequent defuzzification = centroid. Full file: abs_fuzzy_skfuzzy.py
Verification note: scikit-fuzzy could not be installed in the build environment, so the numbers in this deck came from a NumPy re-implementation of the same operations (abs_numpy_check.py). Re-run the .py in your environment to confirm.

## Slide 9: Simulation Interface and Demonstration
DESIGN CONCEPT – not a working simulator
Obstacle distance D (m)
20
Closing speed Vc (m/s)
15
Compute braking
Braking command: [shown after compute]
+ MF and output plots
Fig. 6 – Braking surface (executed model)
Fig. 7 – Output set, D=20, Vc=15
What the genuine plots show
Output stays within 13.3–86.7 % over the whole input grid: centroids of clipped triangles never reach 0 % or 100 %.
Braking rises smoothly toward short distance and high closing speed.
UI status (Phase 6): [pending – insert real Jupyter / Tkinter / Streamlit screenshot here]

## Slide 10: Testing and Results (10 Input Combinations)
ID | D (m) | Vc (m/s) | Expected | Output (%) | Observation
T01 | 5 | 25 | Hard | 84.4 | Near + Fast: Hard, clipped
T02 | 10 | 10 | Hard | 84.4 | Near, partly Moderate: Hard
T03 | 15 | 5 | Moderate | 44.5 | Near/Slow vs Medium/Slow mix
T04 | 20 | 15 | Moderate–Hard | 62.4 | Worked example: Moderate–Hard blend
T05 | 40 | 5 | Light | 15.6 | Medium + Slow: Light
T06 | 40 | 15 | Moderate | 50.0 | Medium + Moderate: peak of Moderate
T07 | 40 | 25 | Hard | 84.4 | Medium + Fast: Hard
T08 | 70 | 5 | Light | 16.3 | Far + Slow: Light
T09 | 70 | 15 | Light | 16.3 | Far + Moderate: Light (same as T08)
T10 | 90 | 28 | Moderate | 50.0 | Far + Fast: Moderate
Chart: Braking output per test (%)
| T01 | T02 | T03 | T04 | T05 | T06 | T07 | T08 | T09 | T10
Braking % | 84.4 | 84.4 | 44.5 | 62.4 | 15.6 | 50 | 84.4 | 16.3 | 16.3 | 50
All outputs lie within 0–100 % and follow the rule base. T08 = T09 because Far gives α = 0.4 in both; the Light set is clipped identically. “Expected” is qualitative; outputs are computed (NumPy equivalent; see slide 8).

## Slide 11: Analysis, Limitations and Future Improvements
Strengths
Readable IF–THEN rules close to human reasoning
Smooth transitions, no abrupt threshold jumps
Easy to tune and extend with more inputs
Limitations observed
Simplified 9-rule base; edge-degenerate MFs
Output limited to 13.3–86.7 % (centroid effect)
Far/Slow and Far/Moderate give identical output
Sensitive to sensor noise in D and Vc
Not modelled
Stopping distance, road friction, tyre grip
Vehicle mass, actuator delay, brake dynamics
Driver intent, road and weather conditions
Future work
Add time-to-collision and acceleration inputs
Validate against a physics-based vehicle model
Compare with PID or tune MFs with a genetic algorithm
Add noise-filtering and a real simulator UI
Proof-of-concept educational simulation – not ready for installation in a real vehicle.

## Slide 12: Conclusion, Status and References
Conclusion
A 9-rule Mamdani FIS maps distance and closing speed to a braking command that rises with urgency across 10 test cases.
Worked example (D=20, Vc=15) gives 62.4 %, between Moderate and Hard as expected.
Unvalidated: real stopping distances, vehicle dynamics, sensor noise, safety certification.
Deliverable | Status
Presentation | This file
Report | [Status to be updated]
Python source | abs_fuzzy_skfuzzy.py (run to confirm)
GitHub repository | [URL]
Short video | [Link]
LinkedIn post | [Link]
References
[1] L.D. College of Engineering, “PBL: Design and Development of a Fuzzy Controller for Real-World Engineering Problem,” BE05000461, course brief, 2026.
[2] scikit-fuzzy developers, “scikit-fuzzy documentation.” https://scikit-fuzzy.github.io/scikit-fuzzy/
[3] L. A. Zadeh, “Fuzzy sets,” Information and Control, vol. 8, no. 3, pp. 338–353, 1965.
[4] E. H. Mamdani and S. Assilian, “An experiment in linguistic synthesis with a fuzzy logic controller,” Int. J. Man-Machine Studies, vol. 7, no. 1, pp. 1–13, 1975.
[5] T. J. Ross, Fuzzy Logic with Engineering Applications, 4th ed. Chichester, U.K.: Wiley, 2016.